| Model | NP-SC6550 |
| --- | --- |
| Tunnel size | 659.4mm Wx504 mm H |
| Conveyor speed | 0.22 m/s |
| Conveyor height | 700mm |
| Max. load | 150 kg (330.69 lb) |
| Penetration (steel) | Standard 8 mm, 11mm by customize |
| Wire resolution | 40AWG |
| Spatial resolution | Vertical: 1.0 mm Horizontal: 1.0 mm |
| X-ray dose per inspection | < 3.5 μSv |
| X-ray leakage | < 1 μSv/h |
| X-ray generator | Anode Voltage: 80 kV, 100% Oil Cooling, Single generator, vertical beam direction. |
| Images colors | B/W, Colors |
| Images storage | 10000 images |
| Film safety | ISO1600 |
| Working temperature | 5 °C to 40 ° C (41 °F to 104 °F) |
| Working humidity | 0% to 90% |
| Operation system | Linux |
| Power supply | AC 220 V (+ 10% to -15%), 50 Hz (±3 Hz) |
| Power consumption | 0.8 kw |
| Dimension (L x W x H) without table | 2195mm x 902 mm x 1362.5 mm (86.42" x 35.51" x 53.64") |
| Weight | 420 kg (925.94lb) |
| Extended table | 614mm |

| Accessories |  |
| --- | --- |
| Extended table | 614mm x1 in exit（Included） |
| LCD monitor | 17” LCD Color Monitor x1 included |
| Dedicated Key board &mouse | Standard included |

# Text boxes

NP-SC6550 X-Ray security inspection system is an advanced security detection system designed for briefcases, postal bags, express mails, hand held parcels, and small packages checking with a world leading x-ray screening and single-energy image processing technology.

With the popular tunnel size of 659mm (W) x 504 (H), compact and movable design, NP-SC6550 is an ideal economical security inspection solution for hotels, government agencies, transportation hubs, logistics industry, courts, prosecutors, prisons, embassies, factories, schools, hospitals, stadiums, exhibition halls, entertainment venues, etc.

NP-SC6550

X-Ray Security Inspection System

Key Features

- High performance with HD image, strong penetration, precise recognition

- Adopts embedded Linux operating system with multi-core ARM

- Energy saving and environment protection with low power consumption

- Supports real-time monitoring

- Supports multiple image processing mode

- Supports POST (power on self-test)

- 64X zoom in

- One-touch power off

- Energy-saving working mode for conveyor available

- Shock-proof design

- User friendly interface for easy operation

System Functions

X-ray Image processing functions:

Color/Black &White, local enhancement, high penetration, low penetration, super enhancement,  inverse color, light increase, light reduce, grey scale scan, image zoom in, edge enhancement.

System functions:

Power on self-diagnosis, multi levels user management, image management, TIP management, curve diagnosis, equipment information query, Multi-format image export, image mirroring, 1-16 times stepless zoom in, operator training, precise positioning of baggage images, clear channel reminder, one key calibration,one-key shutdown

Specifications

Dimension

Available Model

NP-SC6550

Scanned Images

202012